## Slide 1: CHAPTER 4 STRUCTURES
CHAPTER OUTLINE
4/1 Introduction
4/2 Plane Trusses
4/3 Method of Joints
4/4 Method of Sections
4/5 Space Trusses
4/6 Frames and Machines
Myimagefiles/Alamy Stock Photo

## Slide 2: Article 4/1 Introduction
Reminders from Chapter 3
  Equilibrium of a Single Rigid Body
  Free-Body Diagrams of an Entire Structure
  Application of Force and Moment Equations of Equilibrium
Purpose of Chapter 4
  Equilibrium of Several Rigid Bodies
  Free-Body Diagrams of Portions of a Structure
  Application of Force and Moment Equations of Equilibrium
  Application of Newton’s 3rd Law

## Slide 3: Article 4/2 Plane Trusses
Introduction
  Previously, we have been been concerned with the external forces acting on a body. In this section, however, we study the forces internal to a structure. Determining the load on each internal member of a truss or frame allows one to then design that particular member.
Example Bridge Truss
  Each vertical side of the structure is a plane truss, which is a framework composed of members joined at their ends. A simplified model is indicated at the left end of the illustration. The forces L represent the portions of the weights of the roadway, vehicles, stringers, and cross beams which are transferred to the truss joints. Note that joints are modeled as simple pins, even though they might actually be gusset plates or welded connections.

## Slide 4: Article 4/2 – Common Truss Shapes (1 of 2)
Commonly Used Bridge Trusses

## Slide 5: Article 4/2 – Common Truss Shapes (2 of 2)
Commonly Used Roof Trusses

## Slide 6: Article 4/2 – Features of Simple Trusses (1 of 2)
Simple Trusses
  Rigid
  Basic Element
  Two-Force Members
  Weight of Truss Members
  Location of Applied Loads

## Slide 7: Article 4/2 – Features of Simple Trusses (2 of 2)
Simple Trusses (cont.)
  Connections between Members
  Support Representation
The trusses in this text are statically determinant, which means a complete application of Newton’s First Law will provide the solution for all unknown reactions and internal forces. Trusses that cannot be solved in this fashion are statically indeterminate, and information regarding the deformation of the members must be included to obtain the solution.

## Slide 8: Article 4/3 Method of Joints
Features of the Method
  Looks at Equilibrium of Each Joint Connection
  Limited to Force Summation Equations of Equilibrium at each Joint
  Limited to Finding Two Unknown Reactions at a Time
  Proceeds Systematically Across the Truss
  Very Methodical and Easy to Utilize
  Very Useful for Finding all of the Truss-Member Forces

## Slide 9: Article 4/3 – Overview of Method of Joints
General Procedure
  In general, find the external reactions first (this may or may not be necessary).
  Start by analyzing a joint where at least one known applied load acts, and at most, only two unknown truss forces are present.
  Apply a sum of forces in an appropriate x- and y-direction at this joint.
  Draw members in tension or compression, and stay consistent with your choice until you move to the next joint.
  Solve the equilibrium equations for the unknown truss forces.
  Move to the next adjacent joint and repeat the process.

## Slide 10: Article 4/3 – Illustration of Method of Joints (1 of 3)
Determine the force in each member of the truss.
  Determine the external reactions

## Slide 11: Article 4/3 – Illustration of Method of Joints (2 of 3)
Determine the force in each member of the truss.
  Determine the external reactions.
  Start at a joint with only two unknowns, joint A.
  Draw the free-body diagram and apply equilibrium equations.

## Slide 12: Article 4/3 – Illustration of Method of Joints (3 of 3)
Determine the force in each member of the truss.
  Determine the external reactions.
  Start at a joint with only two unknowns, Joint A.
  Draw the free-body diagram and apply equilibrium equations.
  Proceed to the next joint and repeat the process.
  Be careful with the signs of the members and indicate if they are in tension or compression.

## Slide 13: Article 4/3 – Internal and External Redundancy
External Redundancy
Internal Redundancy
Checking for Internal Statical Determinacy
  Number of Internal Members, m
  Number of Joint Connections, j
  Truss is statically determinate internally if… m + 3 = 2j
Comment on Stability

## Slide 14: Article 4/3 – Special Conditions in Trusses (1 of 3)
Condition 1: Three Members at a Joint, Two are Collinear
Condition 2: Two Members at a Joint, Not Collinear

## Slide 15: Article 4/3 – Special Conditions in Trusses (2 of 3)
Condition 3: Two Pairs of Collinear Members at a Joint
Condition 4: Cross Bracing

## Slide 16: Article 4/3 – Special Conditions in Trusses (3 of 3)
Condition 5: Avoiding Simultaneous Equations
  Summing Forces along x-Axis Eliminates F1
  Summing Forces along x′-Axis Eliminates F2

## Slide 17: Article 4/3 – Sample Problem 4/1 (1 of 4)
Problem Statement
  Compute the force in each member of the loaded cantilever truss by the method of joints.

## Slide 18: Article 4/3 – Sample Problem 4/1 (2 of 4)
Find External Reactions

## Slide 19: Article 4/3 – Sample Problem 4/1 (3 of 4)
Equilibrium of Joint A
Equilibrium of Joint B

## Slide 20: Article 4/3 – Sample Problem 4/1 (4 of 4)
Equilibrium of Joint C
Equilibrium of Joint E

## Slide 21: Article 4/3 – Sample Problem 4/2 (1 of 4)
Problem Statement
  The simple truss shown supports the two loads, each of magnitude L. Determine the forces in members DE, DF, DG, and CD.

## Slide 22: Article 4/3 – Sample Problem 4/2 (2 of 4)
Geometry of Joint E
Equilibrium of Joint E

## Slide 23: Article 4/3 – Sample Problem 4/2 (3 of 4)
Geometry of Joint F
Equilibrium of Joint F

## Slide 24: Article 4/3 – Sample Problem 4/2 (4 of 4)
Geometry of Joint D
Equilibrium of Joint D

## Slide 25: Article 4/4 Method of Sections
Differences with the Method of Joints
  Can utilize the moment equation of equilibrium.
  Can analyze an entire section of a truss.
  Can determine the force in almost any desired member directly.
A Word of Caution
  Don’t abandon the method of joints.
  Usually limited to cutting at most three members at one time.

## Slide 26: Article 4/4 – Overview of Method of Sections
General Procedure
  In general, find the external reactions first (this may or may not be necessary).
  If possible, pass a section (or cut) through the desired member and up to two (2) other unknown members, isolating a portion of the truss.
  Apply two-dimensional rigid-body equilibrium equations to the isolated truss portion; e.g., ΣFx = 0, ΣFy = 0, and ΣMO = 0.
  Solve for the unknowns.
  Note that the methods of sections and joints may be used in combination.

## Slide 27: Article 4/4 – Illustration of Method of Sections (1 of 2)
Determine the force in member BE.
  Determine the external reactions.

## Slide 28: Article 4/4 – Illustration of Method of Sections (2 of 2)
Determine the force in member BE.
  Determine the external reactions.
  Pass a section through member BE.
  Choose either side of the truss.
  Apply equilibrium equations.

## Slide 29: Article 4/4 – Additional Considerations
Additional Considerations
  Consider an entire portion of the truss in equilibrium.
  Forces internal to the section are not considered.
  Use either portion of the truss after cutting.
  Combine with method of joints if necessary.
  Select advantageous moment centers.
  Stay mindful of assumed directions for unknown forces, tension or compression.

## Slide 30: Article 4/4 – Sample Problem 4/3 (1 of 3)
Problem Statement
  Calculate the forces induced in members KL, CL, and CB by the 20-ton load on the cantilever truss.

## Slide 31: Article 4/4 – Sample Problem 4/3 (2 of 3)
FBD of Section

## Slide 32: Article 4/4 – Sample Problem 4/3 (3 of 3)
Equilibrium Conditions

## Slide 33: Article 4/4 – Sample Problem 4/4 (1 of 4)
Problem Statement
  Calculate the force in member DJ of the Howe roof truss illustrated. Neglect any horizontal components of force at the supports.

## Slide 34: Article 4/4 – Sample Problem 4/4 (2 of 4)
FBD of Section 1
FBD of Section 2

## Slide 35: Article 4/4 – Sample Problem 4/4 (3 of 4)
Equilibrium Conditions

## Slide 36: Article 4/4 – Sample Problem 4/4 (4 of 4)
Equilibrium Conditions

## Slide 37: Article 4/5 Space Trusses (1 of 2)
Three-Dimensional Analogue of Plane Truss
Basic Shape is a Tetrahedron
Analysis Utilizes Method of Joints and Method of Sections extended to Three Dimensions
Statically Determinant if… m + 6 = 3j

## Slide 38: Article 4/5 Space Trusses (2 of 2)
Method of Joints for Space Trusses
  Same Basic Procedure as for Plane Trusses
  ΣF = 0 at each Joint (ΣFx = 0, ΣFy = 0, and ΣFz = 0)
  Limited to Solving Three (3) Unknown Forces at a Time
Method of Joints for Space Trusses
  Same Basic Procedure as for Plane Trusses
  ΣF = 0 for any Section (ΣFx = 0, ΣFy = 0, and ΣFz = 0)
  ΣM = 0 for any Section (ΣMx = 0, ΣMy = 0, and ΣMz = 0)
  Limited to Solving Six (6) Unknown Forces at a Time

## Slide 39: Article 4/5 – Sample Problem 4/5 (1 of 3)
Problem Statement
  The space truss consists of the rigid tetrahedron ABCD anchored by a ball-and-socket connection at A and prevented from any rotation about the x-, y-, or z-axes by the respective links 1, 2, and 3. The load L is applied to joint E, which is rigidly fixed to the tetrahedron by the three additional links. Solve for the forces in the members at joint E and indicate the procedure for the determination of the forces in the remaining members of the truss.

## Slide 40: Article 4/5 – Sample Problem 4/5 (2 of 3)
Check Determinacy
  m + 6 = 3j
  9 + 6 = 3(5) True
Free-Body Diagram of Joint E

## Slide 41: Article 4/5 – Sample Problem 4/5 (3 of 3)
Equilibrium of Joint E

## Slide 42: Article 4/6 Frames and Machines
Definition
  A structure is called a frame or machine if at least one of its individual members is a multiforce member. A multiforce member is defined as one with three or more forces acting on it, or one with two or more forces and one or more couples acting on it.
Example – Jaws of Life

## Slide 43: Article 4/6 – Types of Structures
Interconnected Rigid Bodies with Multiforce Members
  Rigid Noncollapsible
    Find external reactions for the entire structure first.
    Dismember to find internal reactions.
    Look for two-force members.
  Nonrigid Collapsible
    Dismember the structure first to find internal reactions.
    Compute external reactions later.
    Look for two-force members.

## Slide 44: Article 4/6 – Force Representation and FBDs
Importance of Action-Reaction Pairs
Assumed Force Directions
Vector Notation
Simultaneous Equations

## Slide 45: Article 4/6 – Sample Problem 4/6 (1 of 3)
Problem Statement
  The frame supports the 400-kg load in the manner shown. Neglect the weights of the members compared with the forces induced by the load and compute the horizontal and vertical components of all forces acting on each of the members.

## Slide 46: Article 4/6 – Sample Problem 4/6 (2 of 3)
Free-Body Diagram of Entire Structure (Rigid)
Equilibrium Conditions

## Slide 47: Article 4/6 – Sample Problem 4/6 (3 of 3)
Free-Body Diagrams of Individual Pieces
Equilibrium of Member BF

## Slide 48: Article 4/6 – Sample Problem 4/7 (1 of 4)
Problem Statement
  Neglect the weight of the frame and compute the forces acting on all of its members.

## Slide 49: Article 4/6 – Sample Problem 4/7 (2 of 4)
Free-Body Diagram of Entire Structure (Nonrigid)
Vertical Reactions at A and C

## Slide 50: Article 4/6 – Sample Problem 4/7 (3 of 4)
Free-Body Diagrams of Individual Pieces
Equilibrium of Member ED
F is equal and opposite to E since EF is a two-force member.
Equilibrium of Member AB

## Slide 51: Article 4/6 – Sample Problem 4/7 (4 of 4)
Free-Body Diagrams of Individual Pieces
Equilibrium of Member BC

## Slide 52: Article 4/6 – Sample Problem 4/8 (1 of 3)
Problem Statement
  The machine shown is designed as an overload protection device which releases the load when it exceeds a predetermined value T. A soft metal shear pin S is inserted in a hole in the lower half and is acted on by the upper half. When the total force on the pin exceeds its strength, it will break. The two halves then rotate about A under the action of the tensions in BD and CD, as shown in the second sketch, and rollers E and F release the eye bolt. Determine the maximum allowable tension T if the pin S will shear when the total force on it is 800 N. Also compute the corresponding force on the hinge pin A.

## Slide 53: Article 4/6 – Sample Problem 4/8 (2 of 3)
Individual Free-Body Diagrams
Equilibrium of the Connection D (Note the Symmetry)

## Slide 54: Article 4/6 – Sample Problem 4/8 (3 of 3)
Equilibrium of the Upper Part

## Slide 55: Article 4/6 – Sample Problem 4/9 (1 of 3)
Problem Statement
  In the particular position shown, the excavator applies a 20-kN force parallel to the ground. There are two hydraulic cylinders AC to control the arm OAB and a single cylinder DE to control arm EBIF. (a) Determine the force in the hydraulic cylinders AC and the pressure pAC against their pistons, which have an effective diameter of 95 mm. (b) Also determine the force in hydraulic cylinder DE and the pressure pDE against its 105-mm-diameter piston. Neglect the weights of the members compared with the effects of the 20-kN force.

## Slide 56: Article 4/6 – Sample Problem 4/9 (2 of 3)
Free-Body Diagram of Entire Arm Assembly
Force and Pressure in Cylinder AC

## Slide 57: Article 4/6 – Sample Problem 4/9 (3 of 3)
Free-Body Diagram of Lower Arm
Force and Pressure in Cylinder DE