## Slide 1: CHAPTER 6 FRICTION
CHAPTER OUTLINE
6/1 Introduction
SECTION A Frictional Phenomena
6/2 Types of Friction
6/3 Dry Friction
SECTION B Applications of Friction in Machines
6/4 Wedges
6/5 Screws
6/6 Journal Bearings
6/7 Thrust Bearings; Disk Friction
6/8 Flexible Belts
6/9 Rolling Resistance
Courtesy of Alyse Gagne

## Slide 2: Article 6/1 Introduction
Introduction and Overview

## Slide 3: Article 6/2 Types of Friction
Dry Friction
Fluid Friction
Internal Friction

## Slide 4: Article 6/3 Dry Friction
Mechanism of Dry Friction
  Block on a Rough Surface
  Free-Body Diagram
  Close-Up of Mating Surfaces

## Slide 5: Article 6/3 – Plot of Friction Force
Regions of Significance
  Static Friction Range, F < Fmax
  Impending Motion, F = Fmax = 𝜇sN
  Kinetic Friction, F = Fk = 𝜇kN

## Slide 6: Article 6/3 – Friction Coefficients
Coefficient of Static Friction, 𝜇s
Coefficient of Kinetic Friction, 𝜇k
Table of Values
  Exact values for a specific problem can vary
  significantly from the values presented.

## Slide 7: Article 6/3 – Friction Angles
Static Friction Angle, 𝜙s
  tan 𝜙s = 𝜇s
Kinetic Friction Angle, 𝜙k
  tan 𝜙k = 𝜇k
Friction Cones

## Slide 8: Article 6/3 – Factors Affecting Friction
Contact Area
Molecular Attraction
Temperature
Adhesion
Relative Hardness of Mating Areas
Surface Films

## Slide 9: Article 6/3 – Types of Friction Problems (1 of 2)
Type I: Impending Motion
  Body is on the verge of slipping.
  Equilibrium holds for the body.
  F = Fmax = 𝜇sN
Type II: Relative Motion Exists
  Body is slipping.
  Equilibrium does not hold in the direction of slip.
  F = Fk = 𝜇kN

## Slide 10: Article 6/3 – Types of Friction Problems (2 of 2)
Type III: Unknown – Body may or may not be slipping
  Analysis Steps
    Assume equilibrium of the body.
    Solve for the necessary equilibrium friction force F.
    Check the assumption of equilibrium.
      If F < (Fmax = 𝜇sN):
      Friction force necessary for equilibrium can be supported, and the body is in static equilibrium as assumed. The actual friction force F is less than the limiting value Fmax.
    If F = (Fmax = 𝜇sN):
      Motion is impending, but the assumption of equilibrium still holds.
    If F > (Fmax = 𝜇sN):
    The surfaces cannot support more force than the maximum 𝜇sN, so the assumption of equilibrium is invalid. Motion occurs and F = (Fk = 𝜇kN).

## Slide 11: Article 6/3 – Sample Problem 6/1 (1 of 2)
Problem Statement
  Determine the maximum angle 𝜃 which the adjustable incline may have with the horizontal before the block of mass m begins to slip. The coefficient of static friction between the block and the inclined surface is 𝜇s.

## Slide 12: Article 6/3 – Sample Problem 6/1 (2 of 2)
Equilibrium Conditions

## Slide 13: Article 6/3 – Sample Problem 6/2 (1 of 3)
Problem Statement
  Determine the range of values which the mass m0 may have so that the 100-kg block shown in the figure will neither start moving up the plane nor slip down the plane. The coefficient of static friction for the contact surfaces is 0.30.

## Slide 14: Article 6/3 – Sample Problem 6/2 (2 of 3)
Case I: Motion Impends Up the Plane

## Slide 15: Article 6/3 – Sample Problem 6/2 (3 of 3)
Case II: Motion Impends Down the Plane

## Slide 16: Article 6/3 – Sample Problem 6/3 (1 of 4)
Problem Statement
  Determine the magnitude and direction of the friction force acting on the 100-kg block shown if, first, P = 500 N and, second, P = 100 N. The coefficient of static friction is 0.20, and the coefficient of kinetic friction is 0.17. The forces are applied with the block initially at rest.

## Slide 17: Article 6/3 – Sample Problem 6/3 (2 of 4)
Equilibrium Conditions

## Slide 18: Article 6/3 – Sample Problem 6/3 (3 of 4)
Case I: P = 500 N

## Slide 19: Article 6/3 – Sample Problem 6/3 (4 of 4)
Case II: P = 100 N

## Slide 20: Article 6/3 – Sample Problem 6/4 (1 of 3)
Problem Statement
  The homogeneous rectangular block of mass m, width b, and height H is placed on the horizontal surface and subjected to a horizontal force P which moves the block along the surface with a constant velocity. The coefficient of kinetic friction between the block and the surface is 𝜇k. Determine (a) the greatest value which h may have so that the block will slide without tipping over and (b) the location of a point C on the bottom face of the block through which the resultant of the friction and normal forces acts if h = H/2.

## Slide 21: Article 6/3 – Sample Problem 6/4 (2 of 3)
Part (a) Maximum Value of h

## Slide 22: Article 6/3 – Sample Problem 6/4 (3 of 3)
Part (b) h = H/2

## Slide 23: Article 6/3 – Sample Problem 6/5 (1 of 4)
Problem Statement
  The three flat blocks are positioned on the 30° incline as shown, and a force P parallel to the incline is applied to the middle block. The upper block is prevented from moving by a wire which attaches it to the fixed support. The coefficient of static friction for each of the three pairs of mating surfaces is shown. Determine the maximum value which P may have before any slipping takes place.

## Slide 24: Article 6/3 – Sample Problem 6/5 (2 of 4)
Free-Body Diagrams
Normal Force Calculations

## Slide 25: Article 6/3 – Sample Problem 6/5 (3 of 4)
Assume 50-kg Block Slips

## Slide 26: Article 6/3 – Sample Problem 6/5 (4 of 4)
Check Assumption
Revise Calculation for P

## Slide 27: Article 6/4 Wedges
Overview and Illustration

## Slide 28: Article 6/4 – Raising a Load
Free-Body Diagrams
Wedge Angle, α
Force Polygons

## Slide 29: Article 6/4 – Lowering a Load
Free-Body Diagrams
Wedge Angle, α
Force Polygons

## Slide 30: Article 6/4 – Self-Locking of a Wedge (1 of 2)
Explanation of Self-Locking
Impending Slip at the Upper Surface

## Slide 31: Article 6/4 – Self-Locking of a Wedge (2 of 2)
Impending Slip at the Lower Surface
Range for No Slip

## Slide 32: Article 6/5 Screws
Introduction
Force Analysis
Applied Moment, M = Wr tan (α + 𝜙)
Lead, L
Helix Angle, tan α = L/2πr

## Slide 33: Article 6/5 – Unwrapped Thread View
Applied Moment, M = Wr tan (α + 𝜙)
Helix Angle, tan α = L/2πr
Equivalent Force, P = M/r

## Slide 34: Article 6/5 – Conditions for Unwinding
Case I: α < 𝜙
Case II: α > 𝜙

## Slide 35: Article 6/5 – Sample Problem 6/6 (1 of 4)
Problem Statement
  The horizontal position of the 500-kg rectangular block of concrete is adjusted by the 5° wedge under the action of the force P. If the coefficient of static friction for both wedge surfaces is 0.30 and if the coefficient of static friction between the block and the horizontal surface is 0.60, determine the least force P required to move the block.

## Slide 36: Article 6/5 – Sample Problem 6/6 (2 of 4)
Solution

## Slide 37: Article 6/5 – Sample Problem 6/6 (3 of 4)
Algebraic Solution

## Slide 38: Article 6/5 – Sample Problem 6/6 (4 of 4)
Graphical Solution

## Slide 39: Article 6/5 – Sample Problem 6/7 (1 of 4)
Problem Statement
  The single-threaded screw of the vise has a mean diameter of 1 in. and has 5 square threads per inch. The coefficient of static friction in the threads is 0.20. A 60-lb pull applied normal to the handle at A produces a clamping force of 1000 lb between the jaws of the vise. (a) Determine the frictional moment MB, developed at B, due to the thrust of the screw against the body of the jaw. (b) Determine the force Q applied normal to the handle at A required to loosen the vise.

## Slide 40: Article 6/5 – Sample Problem 6/7 (2 of 4)
Equilibrium of the Jaw

## Slide 41: Article 6/5 – Sample Problem 6/7 (3 of 4)
(a) To Tighten

## Slide 42: Article 6/5 – Sample Problem 6/7 (4 of 4)
(b) To Loosen

## Slide 43: Article 6/6 Journal Bearings
Purpose
Illustration
Load Analysis
Torque to Maintain Rotation
  M = Lr sin 𝜙 = μLr

## Slide 44: Article 6/7 Thrust Bearings; Disk Friction
Purpose
Example
Westend61 GmbH/Alamy Stock Photo

## Slide 45: Article 6/7 – Disk Friction Load Analysis
Free-Body Diagram
  Axial Force, P
  Transmitted Torque, M
  Pressure Between the Plates, p = P/πR2
Friction Force on a Differential Area
  dF = μp dA
Integration over the Disk Area
  M = 2/3 μPR

## Slide 46: Article 6/7 – Collar Bearing Load Analysis
Example with a Collar Bearing
  Inside Contact Radius, Ri
  Outside Contact Radius, Ro
Integration over the Disk Area
  M = 2/3 μP(Ro3 - Ri3)/(Ro2 - Ri2)

## Slide 47: Article 6/7 – Effect of Wear-In
Solid Disks
  M = 1/2 μPR
Ring Disks
  M = 1/2 μP(Ro + Ri)

## Slide 48: Article 6/7 – Sample Problem 6/8 (1 of 4)
Problem Statement
  The bell crank fits over a 100-mm-diameter shaft which is fixed and cannot rotate. The horizontal force T is applied to maintain equilibrium of the crank under the action of the vertical force P = 100 N. Determine the maximum and minimum values which T may have without causing the crank to rotate in either direction. The coefficient of static friction 𝜇 between the shaft and the bearing surface of the crank is 0.20.

## Slide 49: Article 6/7 – Sample Problem 6/8 (2 of 4)
Solution

## Slide 50: Article 6/7 – Sample Problem 6/8 (3 of 4)
Impending Counterclockwise Motion

## Slide 51: Article 6/7 – Sample Problem 6/8 (4 of 4)
Impending Clockwise Motion

## Slide 52: Article 6/8 Flexible Belts
Introduction
Illustration
© Media Bakery

## Slide 53: Article 6/8 – Derivation (1 of 2)
Situation of Interest
Free-Body Diagram of a Belt Segment

## Slide 54: Article 6/8 – Derivation (2 of 2)
Equilibrium Conditions
Combine and Integrate
  dT/T = μ dθ → T2 = T1eμβ

## Slide 55: Article 6/8 – The Belt Friction Equation
Comments about the Equation: T2 = T1eμβ
  T2 = the larger of the two belt tensions (it points in the direction the belt will tend to move in along the surface).
  T1 = the smaller of the two belt tensions (it opposes the motion of the belt along the surface).
  μ = the coefficient of friction between the belt and the surface.
  β = the total angle of belt contact with the surface. It must be expressed in radians.

## Slide 56: Article 6/9 Rolling Resistance
Introduction
Illustration
Load Analysis
  Load on the Wheel, L
  Force to Maintain Speed, P
  Distribution of Pressure over the Contact Area, p
  Resultant Pressure-Force Distribution, R
  Location of Resultant Pressure Force, A
  Forward Shift of the Pressure Center from the Wheel Center, a

## Slide 57: Article 6/9 – Load Analysis
Moment Sum about the Pressure Center
  P = a/rL = μrL
Coefficient of Rolling Resistance, μr

## Slide 58: Article 6/9 – Sample Problem 6/9 (1 of 3)
Problem Statement
  A flexible cable which supports the 100-kg load is passed over a fixed circular drum and subjected to a force P to maintain equilibrium. The coefficient of static friction 𝜇 between the cable and the fixed drum is 0.30. (a) For 𝛼 = 0, determine the maximum and minimum values which P may have in order not to raise or lower the load. (b) For P = 500 N, determine the minimum value which the angle 𝛼 may have before the load begins to slip.

## Slide 59: Article 6/9 – Sample Problem 6/9 (2 of 3)
Part (a) α = 0

## Slide 60: Article 6/9 – Sample Problem 6/9 (3 of 3)
Part (b) P = 500 N

## Slide 61: Article 6/9 – Sample Problem 6/10 (1 of 4)
Problem Statement
  Determine the range of mass m over which the system is in static equilibrium. The coefficient of static friction between the cord and the upper curved surface is 0.20, while that between the block and the incline is 0.40. Neglect friction at the pivot O.

## Slide 62: Article 6/9 – Sample Problem 6/10 (2 of 4)
Equilibrium of Slender Bar

## Slide 63: Article 6/9 – Sample Problem 6/10 (3 of 4)
Case I: Motion Impends Up the Incline

## Slide 64: Article 6/9 – Sample Problem 6/10 (4 of 4)
Case II: Motion Impends Down the Incline