## Slide 1: CHAPTER 7 VIRTUAL WORK
CHAPTER OUTLINE
7/1 Introduction
7/2 Work
7/3 Equilibrium
7/4 Potential Energy and Stability
BuildPix/(c)Construction Photography/Photoshoot

## Slide 2: Article 7/1 Introduction
Introduction

## Slide 3: Article 7/2 Work
Work of a Force
  Illustration
  Calculation
    U = (F cos α )Δs = F (Δs cos α)
  Scalar Quantity

## Slide 4: Article 7/2 – Sign Convention
Positive Work
  Working component of F is in the same direction as the displacement.
Negative Work
  Working component of F is in the opposite direction as the displacement.

## Slide 5: Article 7/2 – General Situation
General Illustration of Work by a Force
General Expression for Work by a Force
  dU = F·dr

## Slide 6: Article 7/2 – Work of a Couple
General Illustration of Work by a Couple
General Expression for Work by a Couple
  dU = M dθ
Sign Convention
  Positive if couple acts in the same sense as rotation.
  Negative if couple acts in the opposite sense as rotation.

## Slide 7: Article 7/2 – Dimensions and Units of Work
Dimensions
  (Force) × (Distance)
SI Units
  Joule (J)
  J = N·m
U.S. Customary Units
  foot-pound (ft-lb)
  Not to be confused with moment which is pound-foot (lb-ft) and a vector quantity, whereas work is a scalar quantity.

## Slide 8: Article 7/2 – Virtual Work
Virtual Displacement
  Does not actually exist, but is assumed to exist.
  Infinitesimal in size.
  Consistent with the constrains of the system.
  Instantaneous in time.
Virtual Work done by a Force and Couple
  δU = F·dr or δU = F δs cos α
  δU = M δθ

## Slide 9: Article 7/3 Equilibrium
Equilibrium of a Particle
Virtual Work done on the Particle
Scalar Expression of Virtual Work
Result

## Slide 10: Article 7/3 – Equilibrium of a Rigid Body
Equilibrium of a Rigid Body
Determine the Roller Force, R
Virtual Work Calculation
  δU = 0 = Rb δθ - Pa δθ
Result
  Pa - Rb = 0
  Equivalent to Moment Summation about Hinge O

## Slide 11: Article 7/3 – Equilibrium of Ideal Systems of Rigid Bodies
Ideal System
  Friction is Neglected
  Connections do not Absorb Energy
Example
Active Forces
  Perform Virtual Work

## Slide 12: Article 7/3 – Other Types of Forces to Consider
Reactive Forces
  Act at Fixed Locations
  Do not Perform Virtual Work
Internal Forces
  Occur in Equal and Opposite Pairs
  Net Virtual Work is Zero

## Slide 13: Article 7/3 – Principle of Virtual Work (1 of 2)
The Principle Stated
  The virtual work done by external active forces on an ideal mechanical system in equilibrium is zero for any and all virtual displacements consistent with the constraints.
Mathematical Expression
  δU = 0

## Slide 14: Article 7/3 – Principle of Virtual Work (2 of 2)
Advantages of Virtual Work
  It is not necessary to dismember ideal systems to establish the relations between active forces.
  The relations between active forces may be determined directly without reference to the reactive forces.
General Comments
  Method of virtual work requires internal friction forces do negligible work, or else the work by friction must be considered.
  Construct an active-force diagram which shows only the active forces which act on the body. The reactive forces and internal forces do not perform any virtual work and do not need to be included.

## Slide 15: Article 7/3 – Degrees of Freedom (1 of 2)
Definition
  The number of degrees of freedom of a mechanical system is the number of independent coordinates needed to specify completely the configuration of the system.
  The principle of virtual work may be applied as many times as there are degrees of freedom.
  With each application, allow only one independent coordinate to change at a time while holding the others constant.
One-Degree-of-Freedom Systems

## Slide 16: Article 7/3 – Degrees of Freedom (2 of 2)
Two-Degree-of-Freedom Systems

## Slide 17: Article 7/3 – Systems with Friction (1 of 2)
Effect of Friction
  Dissipates Positive Work by External Forces
  Negative Work which cannot be Regained
Illustration with Sliding Block
Situation of a Rolling Wheel

## Slide 18: Article 7/3 – Systems with Friction (2 of 2)
Friction at a Pinned Connection

## Slide 19: Article 7/3 – Mechanical Efficiency (1 of 3)
Efficiency Defined
  Efficiency is the ratio of the output work from a machine and the input work to the machine.
Mathematical Expression

## Slide 20: Article 7/3 – Mechanical Efficiency (2 of 3)
Example 1: Block Moving up an Incline
Efficiency

## Slide 21: Article 7/3 – Mechanical Efficiency (3 of 3)
Example 2: Screw Jack
Efficiency

## Slide 22: Article 7/3 – Sample Problem 7/1 (1 of 3)
Problem Statement
  Each of the two uniform hinged bars has a mass m and a length l, and is supported and loaded as shown. For a given force P determine the angle 𝜃 for equilibrium.

## Slide 23: Article 7/3 – Sample Problem 7/1 (2 of 3)
Solution

## Slide 24: Article 7/3 – Sample Problem 7/1 (3 of 3)
Solution (cont.)

## Slide 25: Article 7/3 – Sample Problem 7/2 (1 of 3)
Problem Statement
  The mass m is brought to an equilibrium position by the application of the couple M to the end of one of the two parallel links which are hinged as shown. The links have negligible mass, and all friction is assumed to be absent. Determine the expression for the equilibrium angle 𝜃 assumed by the links with the vertical for a given value of M. Consider the alternative of a solution by force and moment equilibrium.

## Slide 26: Article 7/3 – Sample Problem 7/2 (2 of 3)
Solution

## Slide 27: Article 7/3 – Sample Problem 7/2 (3 of 3)
Solution (cont.)

## Slide 28: Article 7/3 – Sample Problem 7/3 (1 of 3)
Problem Statement
  For link OA in the horizontal position shown, determine the force P on the sliding collar which will prevent OA from rotating under the action of the couple M. Neglect the mass of the moving parts.

## Slide 29: Article 7/3 – Sample Problem 7/3 (2 of 3)
Solution

## Slide 30: Article 7/3 – Sample Problem 7/3 (3 of 3)
Solution (cont.)
Thus,

## Slide 31: Article 7/4 Potential Energy and Stability
Elastic Potential Energy
Illustration
  Linear Spring Stiffness, k
  Spring Force, F = kx
  Work done on the Spring, dU = F dx
  Potential Energy, Ve = ½ kx2
  Change in Potential Energy, ΔVe = ½ k(x22 - x12)

## Slide 32: Article 7/4 – Elastic Potential Energy (cont.)
Virtual Displacements and Potential Energy
  Virtual Displacement, δx
  Virtual Change in Potential Energy, δVe = F δx
Sign Convention
  If the spring is compressed, the virtual change in elastic potential energy is negative.
  If the spring is stretched, the virtual change in elastic potential energy is positive.
The work done on the body is the negative of the potential energy change of the spring.

## Slide 33: Article 7/4 – Torsional Springs
A torsional spring resists rotation of a shaft or another element.
Torsional Stiffness, kT
  Units of torque per radian twist (N·m/rad or lb-ft/rad)
Elastic Potential Energy, Ve = ½ kTθ2

## Slide 34: Article 7/4 – Gravitational Potential Energy (1 of 3)
Illustration & Definition
  The gravitational potential energy Vg is defined as the work done on the body by a force equal and opposite to the weight in bringing the body to the position under consideration from some arbitrary datum plane where the potential energy is defined to be zero.
Potential Energy, Vg = mgh
  Height h is measured from the datum.
  Above the datum is considered positive.
  Below the datum is considered negative.
Change in Potential Energy, ΔVg = mg Δh

## Slide 35: Article 7/4 – Gravitational Potential Energy (2 of 2)
Path Irrelevance

## Slide 36: Article 7/4 – Gravitational Potential Energy (3 of 3)
Virtual Displacements and Potential Energy
  Virtual Displacement, δh
  Virtual Change in Potential Energy, δVg = mg δh
Sign Convention
  If the virtual displacement is upward, the sign of the virtual change in gravitational potential energy is positive.
  If the virtual displacement is downward, the sign of the virtual change in gravitational potential energy is negative.
The work done on the body is the negative of the potential energy change of the body.

## Slide 37: Article 7/4 – The Principle of Virtual Work Restated
The Equation Restated
  The virtual work done by all external active forces (other than the gravitational and spring forces accounted for in the potential energy terms) on a mechanical system in equilibrium equals the corresponding change in the total elastic and gravitational potential energy of the system for any and all virtual displacements consistent with the constraints.
Mathematical Expression: δU′ – (δVe + δVg) = 0 or δU′ = δV
  δU′ = sum of the work done by all active forces other than springs or weight.
  -δVe = work done by the spring forces.
  -δVg = work done by the weight forces.
  δV = change in total elastic and gravitational potential energy of the system.
  The equation above is also called the energy equation.

## Slide 38: Article 7/4 – Active Force Diagrams
Illustration
  (a) Body of Interest
  (b) Use of Equation 7/3
  (c) Use of Equation 7/6

## Slide 39: Article 7/4 – Stability of Equilibrium (1 of 2)
Introduction
  Consider a mechanical system where movement is accompanied by changes in gravitational and elastic potential energies and where no work is done on the system by nonpotential forces (δU′ = 0).
  δU′ - (δVe + δVg) = 0 or (δVe + δVg) = 0 or δ (Ve + Vg) = 0 or δV = 0
  The total potential energy V of the system is constant or has a stationary value.
One-Degree-of-Freedom System Implication
  Potential energy is a function of some variable, x, and its derivatives.
  Then…dV/dx = 0 for equilibrium.

## Slide 40: Article 7/4 – Stability of Equilibrium (2 of 2)
Conditions on Equilibrium
  Stable: Total Potential Energy is a Minimum
  Unstable: Total Potential Energy is a Maximum
  Neutral: Total Potential Energy is a Constant
  Mathematical Summary

## Slide 41: Article 7/4 – Sample Problem 7/4 (1 of 3)
Problem Statement
  The 10-kg cylinder is suspended by the spring, which has a stiffness of 2 kN/m. Plot the potential energy V of the system and show that it is minimum at the equilibrium position.

## Slide 42: Article 7/4 – Sample Problem 7/4 (2 of 3)
Solution

## Slide 43: Article 7/4 – Sample Problem 7/4 (3 of 3)
Solution (cont.)

## Slide 44: Article 7/4 – Sample Problem 7/5 (1 of 3)
Problem Statement
  The two uniform links, each of mass m, are in the vertical plane and are connected and constrained as shown. As the angle 𝜃 between the links increases with the application of the horizontal force P, the light rod, which is connected at A and passes through a pivoted collar at B, compresses the spring of stiffness k. If the spring is uncompressed in the position where 𝜃 = 0, determine the force P which will produce equilibrium at the angle 𝜃.

## Slide 45: Article 7/4 – Sample Problem 7/5 (2 of 3)
Solution

## Slide 46: Article 7/4 – Sample Problem 7/5 (2 of 3)
Solution (cont.)

## Slide 47: Article 7/4 – Sample Problem 7/6 (1 of 4)
Problem Statement
  The ends of the uniform bar of mass m slide freely in the horizontal and vertical guides. Examine the stability conditions for the positions of equilibrium. The spring of stiffness k is undeformed when x = 0.

## Slide 48: Article 7/4 – Sample Problem 7/6 (2 of 4)
Solution

## Slide 49: Article 7/4 – Sample Problem 7/6 (3 of 4)
Stability Equation
Stability Solution I

## Slide 50: Article 7/4 – Sample Problem 7/6 (3 of 4)
Stability Solution II